## Slide 1: Solibri Rulesets

## Slide 2: Solibri Rulesets
What do I need to check?
I need to check the agreed deliverables from the model, generally coordination and data
Should I check anything else?
Nope!
How should I communicate the results?
Through open standards such as BCF files. And progress markers.
When do I check?
At each model upload.
How?

## Slide 3: Solibri Rulesets
Clash detection.
Is this thing touching that thing
The best way is the easiest way and the most easily repeatable way
Archi Vs Archi
Structural Vs Structural
MEP Vs MEP
Landscape Vs Landscape
Archi Vs Structural
Archi Vs MEP
Archi Vs Landscape
Structural Vs MEP
Structural Vs Landscape
Landscape Vs MEP

## Slide 4: Solibri Rulesets
So Archi Vs Archi is my first check
The standard rule check is this
Exclude spaces and openings, and use 25mm tolerance *

## Slide 5: Solibri Rulesets
But my report gives me useless data
Its just overall numbers
It doesn’t tell me anything

## Slide 6: Solibri Rulesets
There has to be a better way to do Archi Vs Archi
Looking at the Archi component list there are 19 components I care about.
Excluding ‘Opening’ and ‘Space’.
If I spent some time breaking down the rules then would I have usable data

## Slide 7: Solibri Rulesets
Every component against every other component
Formatted to exclude duplicates by just removing them. No exclusions
My report should look a little different now

## Slide 8: Solibri Rulesets
I now have a component by component report
And it does……
Which is handy if I want to communicate

## Slide 9: Solibri Rulesets
Plug this detailed data into Power Bi and the data can tell a story
The client doesn’t care about numbers. They want to be informed. What, when, who, why. How do we address the trend
Chart: Archi Clashes
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
 | 200 | 225 | 350 | 250 | 200 | 150 | 125 | 200 | 110 | 140 | 140 | 190
Chart: Slab Clashes
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
 | 150 | 150 | 350 | 190 | 50 | 75 | 100 | 190 | 150 | 100 | 100 | 40
Chart: Slab Vs Wall
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
 | 50 | 150 | 350 | 220 | 25 | 25 | 40 | 120 | 120 | 75 | 100 | 40

## Slide 10: Solibri Rulesets
Ive done this for every clash check that could ever be…….
Archi Vs Archi
Structural Vs Structural
MEP Vs MEP
Landscape Vs Landscape
Archi Vs Structural
Archi Vs MEP
Archi Vs Landscape
Structural Vs MEP
Structural Vs Landscape
Landscape Vs MEP
There are over 4000 rules for MEP Vs MEP, at least 10,000 rules in total. Time consuming to write them???

## Slide 11: Solibri Rulesets
It would take months to create 10,000 rules
I used a mouse recorder to do it for me

## Slide 12: Solibri Rulesets
Tolerances.
Sometimes tolerances need to be appropriate to the components
These clashes don’t show at 25mm
Adjust to suit.

## Slide 13: Solibri Rulesets
So that’s clashes covered.
What about non clashes
Everything in every building touches something. Nothing floats.
I have to find the floaters, and graph them.

## Slide 14: Solibri Rulesets
How do you find things that don’t touch other things
You need a rule within a rule within a rule. A triple gateway rule

## Slide 15: Solibri Rulesets
1st Rule
Find things that don’t clash

## Slide 16: Solibri Rulesets
2nd Rule
Of the non clashers which ones are not touching perfectly

## Slide 17: Solibri Rulesets
3rd Rule Show the items
The rule takes hours to check every possible floater, so possibly target the component types you are interested it

## Slide 18: Solibri Rulesets
Clashes and non clashes done.
Some basic coordination checks to add……
Door swings.
Containment space
Lintel clashes
Others
Others
Others

## Slide 19: Solibri Rulesets
Clashes and non clashes done.
Basic coordination checks done
Data checks to do……….
Predefined Type
Uniclass
COBie

## Slide 20: Solibri Rulesets
Data can be done by checking that components have data from an agreed list

## Slide 21: Solibri Rulesets
Plugging this list into Solibri allows me to identify any component with a property not on the list

## Slide 22: Solibri Rulesets
Same for Uniclass………. For every component. Ongoing

## Slide 23: Solibri Rulesets
Same for COBie……………To do

## Slide 24: Solibri Rulesets
And all of these data checks can be fed to Power Bi too
Trustworthy, easy, repeatable, trackable and presentable checks.
In client friendly graphs